## Slide 1: Principles of Lean Enterprise
Presenter: Instructors Name

## Slide 2: Course Outline
Know the definition of lean
Understand the difference between value added and non-value added
Develop an awareness of unevenness, overburden, and the 8 wastes
Discover several lean tools
Learn the principle of respect for people and the problem of underutilized creativity
Build awareness of push and pull workflow

## Slide 3: SIMULATION Round 1

## Slide 4: Rules
Positions Needed: timer, material handler, warehouse manager, assemblers & a recorder
Build trucks in batches of 5, but keep building
Use boxes, get enough parts for 5 trucks from Warehouse
Material Handler only moves batch of 5 trucks to next operation
Each Assembler then gets more parts
Build as fast as you can (more parts = more pay!)
Head down, no talking
You have 10 months (minutes) to build 40 trucks
The Boss is always right!

## Slide 5: De-Brief
How did it feel?
What can we do better? How?
How did we do financially?
Breakdown Simulation

## Slide 6: LEAN
The systematic and relentless elimination of waste in all its forms in pursuit of…
The Best Quality
Lowest Cost
Shortest Lead Time
Best safety
Highest morale
Respect for people
Continuous Improvement
Notes: SYSTEMATIC
RELENTLESS
ELIMINATION
= INTENTIONAL

## Slide 7: Define VALUE ADDED
Value added activities change the market form or function of the product or service
Non value added activities DO NOT change the market form or function of the product or service

## Slide 8
How much time do you think is spent on non-value added activities?
?
Q:
Chart: 
| Non Value added Activities | Value added activities
Sales | 50 | 50
?

## Slide 9
Typical value added percentage of lead time:
Chart: 
| Non Value added Activities | Value added activities
Sales | 95 | 5
A:

## Slide 10: 8 Wastes
Over Production
Excess Inventory
Excess Transportation
Excess Motion
Over Processing
Defects
Waiting
Underutilized Talent

## Slide 11
Over
Production
Producing more than what is needed by the next process or customer. (Too much, too soon, too fast)

## Slide 12
Excess
Inventory
Excess raw materials, work in progress,
and finished goods

## Slide 13
Excess
Transportation
Moving product from one
place to another

## Slide 14
Excess
Motion
Excessive human movement such
as searching, reaching, or stacking

## Slide 15
Over
Processing
Taking unneeded steps to produce
or modify a product

## Slide 16
Defects
Producing defective product
or correcting work already done
(rework)

## Slide 17
Waiting
Time spent with no activity taking place –
people waiting for parts, machines, information
or supplies

## Slide 18
Under
Utilized Talent
Underutilizing people’s
knowledge and creativity
in the workplace

## Slide 19: Underutilized Creativity
We want to not only show respect to our people, the same way we want to show respect to everyone we meet in life, we also want to respect their humanity, what it is that makes us human, which is our ability to think and feel – we have to respect that humanity in the way we design the work, so that the work enables their very human characteristics to flourish.
“
“
FUJO CHO – Toyota Motor Company

## Slide 20: Wastes are symptoms of problems
Lean tools make the problems visible to the organization

## Slide 21: Simulation Round 2
What improvements
would you like to
make?
Notes: Class makes suggestions on changes with limitations from instructor
Some movement of work stations, but not all
Can reduce batch size to 3
Same work instructions as Round 1 for each station

## Slide 22: Lean Building Blocks – House of Lean
Quick Set-up
Standardized Work
Lot Size Reduction
Teams
Quality at Source
5S System
Visual
Plant Layout
POUS
Cellular Flow
Pull / Kanban
TPM
Value
Stream
Mapping
Continuous Improvement
+ HUNDREDS MORE!
Notes: Purpose: Introduce the “House of Lean”
Main point:
All of these tools are used in lean manufacturing.
Many of them utilize the same principles and build upon each other
The goal is to eliminate wastes and implement flow

## Slide 23: Standardized Work
Consistent
Process
Desired
Results
Defines operations safely carried out with all tasks organized in the best known sequence using the most effective combination of these resources:
People
Materials
Methods
Machines
Inconsistent
Process
Inconsistent
Results
Without Standardized Work – there can be no sustained improvements
Implementing Lean: Part I
Notes: Purpose: Introduce the concept of Standardized work
Main point:
Traditional manufacturing view would be to maximize one of these elements.
Without a standard there will always be inefficient variation.
This is a necessary foundation / ground level activity for lean manufacturing
Standardized work is a major component of any quality system: ISO, QSR, Malcolm Baldridge
Once we have figured out the best way we always do it in that exact manner until an even better way is discovered
Finding a better way is always controlled and measured.

## Slide 24: Workplace Organization (5S)
Creates a safe, clean, neat arrangement of the workplace
Provides a specific location for everything
Eliminates anything not required.
Notes: Purpose: Emphasize that organization of a workplace is critical to implementation of lean
Main point:
“A place for everything and everything in its place”
It is much easier to find things if you know where to look for them
This is the impression you leave with customers and suppliers of your product when they visit your factory.

## Slide 25: Elements of a 5S Program
5. Sustain
1. Sort
4. Standardize
3. Shine
2. Set in Order
Notes: Purpose: Introduce the 5S program
Main point:
The 5S program is merely a way to implement good housekeeping practices
Don’t get hung up on what the S’s stand for, the basics are the same
Sort – Remove all unnecessary items such as racks, tools, containers, equipment and excess materials
Set in Order – Put what is left in order. Designate locations, use shadow boards, if there is not a designated space for something it doesn’t belong in the area.
Shine – Clean up what it left. Paint it, refurbish it, etc. Get the remaining items into the same condition as when they were new. A clean work place is much more pleasant to work in; employee morale may even be improved.
Standardize – Develop procedures that can keep things “like new”, for example house keeping and preventative maintenance. Assign responsibilities to apply these procedures. Get “affected” workgroups to make sure procedures are being utilized.
Sustain – This is the most difficult part. Don’t cut corners. Stick to the standards you develop.
This is not easy. How difficult is it to get your child to keep their room clean?

## Slide 26: Visual Controls
Simple signals that:
provide immediate understanding of a situation / condition
are efficient, self-regulating, and worker-managed
Cleaning Station
(Is anything missing?)
Notes: Purpose: Introduce the concept of visual controls and the power of using them
Main point:
Visual controls are waste elimination tools. They should be designed to quickly provide useful information.
They should be designed to indicate that a normal or abnormal condition exists
Examples - Color coded dies, tools and pallets - Lines on the floor to delineate storage areas, walk ways or work areas - Red / Yellow / Green indicators painted on the wall to indicate inventory levels - Cleaning station shadow board – is anything missing?
Operators don’t have to print a report or have some one tell them what to do.

## Slide 27: Visual Controls
Example: Inventory Management
Green = inventory levels are acceptable
Yellow = inventory is getting low (Re-order next cycle)
Red = inventory is below minimum set levels (Re-order now!)
Notes: Purpose: Introduce the concept of visual controls and the power of using them
Main point:
Visual controls are waste elimination tools. They should be designed to quickly provide useful information.
They should be designed to indicate that a normal or abnormal condition exists
Examples - Color coded dies, tools and pallets - Lines on the floor to delineate storage areas, walk ways or work areas - Red / Yellow / Green indicators painted on the wall to indicate inventory levels - Cleaning station shadow board – is anything missing?
Operators don’t have to print a report or have some one tell them what to do.

## Slide 28: Plant Layout
Raw Stock
Ship
Shear
QC
Stamp
Assembly
Brake
Mill
Weld
Grind
Parts Stock
QC
Rec
Screw Machine
Lathe
Finish
Drill
Notes: Purpose: Reinforce that plant layout can drive a lot of waste
Main point:
Traditional plant layouts are “functional” in nature.
They usually become departmentalized which does not promote good communication and team work.
They are usually organized by function or machines with no strategy for flowing product through the factory.
People can put a lot of “mileage” on the product as it weaves its way through the factory.
What if we discover a problem in assembly that was caused in stamping? It probably happened weeks ago, is any one going to remember?

## Slide 29: Teams
Teams
Members rotate between highly specified jobs.
Cross-trained and multi-skilled employee
Work to develop operators who can work many operations within a cell and operations in different cells.
A foundation of the continuous
improvement philosophy
Notes: Purpose: Introduce the concept of teams
Main point:
Team environments are critical to the success of Lean Manufacturing.
Cross training provides an overlap of skill sets. Companies are vulnerable if they rely on a few key people to know how to do a job.
It is critical that management fosters an environment that supports participatory decision making.

## Slide 30: Impact of Size reduction
5 minutes
5 minutes
Lead Time:
15+ minutes for total order
11+ minutes for first piece
5 minutes
Process
A
Process
B
Process
C
Small Lot Production
Process
A
10 minutes
10 minutes
Lead Time:
30+ minutes for total order
21+ minutes for first piece
10 minutes
Process
B
Process
C
Large Batch & Queue Processing

## Slide 31: Set-Up Time Definition
Set-up
time
Changeover
Locate tools, dies or fixtures
Detach & attach tools, dies or fixtures
Run
Part
Run
Part
Completion
of the first
good part
Make Adjustments
Make Adjustments
Completion of last good part
1st Piece Inspection
The time between the last good piece off the current run and the first good piece off the next run.
Notes: Purpose: Introduce the concept of Set-up reduction and define Set-up
If a good part is produced with no adjustments, the run time is not part of the setup time
Main point:
Most companies focus on change over improvements where this is just a small fraction of the time invested in equipment set-up.
We have learned about standardization, How does this tie into controlling and improving set-up times?
Can any of these set-up activities be done while the machine is still running? Challenge the traditional way of setting up a machine.
SMED & FAST approach to set-up reduction.

## Slide 32: Point Of Use Storage (POUS)
Before POUS
Notes: Purpose: Introduce the concept of Point Of Use Storage (POUS)
Main point:
Eliminates much of the wait associated with movement.
Can eliminate or minimize counting.
Operators are not waiting on material from the warehouse or having to go get more.
Operators are not looking around for tooling.

## Slide 33: POUS (Continued)
Raw material is stored at workstation where used
Simplifies physical inventory tracking, storage, and handling
For outside suppliers - works best if vendor relationship permits frequent, on-time, small shipments
Notes: Purpose: Introduce the concept of Point Of Use Storage (POUS)
Main point:
Eliminates much of the wait associated with movement.
Can eliminate or minimize counting.
Operators are not waiting on material from the warehouse or having to go get more.
Operators are not looking around for tooling.

## Slide 34: Quality at the Source
Source Inspection:
Operators only pass work of acceptable quality to next work station.
Visual Tools:
Use samples, pictures, templates or established standards.
Tools and Training:
Give operators the tools and training to perform inspection at the source before they pass it along.
Notes: Purpose: Explain Quality at the source
Main point:
Operators have a clear understanding of what is good and bad.
Root cause of defects are forced to the surface and can be addressed.
The focus is on quality not speed.
Quality can be a moving target depending upon where you are in the month.

## Slide 35: Total Productive Maintenance
Eliminating the six major equipment losses:
Startup
Set-up & adjustment
Idling & minor stoppages
Reduced speed
Breakdowns
Defects & rework
How?
Analyze equipment performance
Identify root cause of problem
Implement sustainable improvements
Notes: Purpose: Discuss Total Productive Maintenance (TPM)
Main point:
The simulation does not touch on this subject but it is an important part of maintaining flow.
Consistent and reliable equipment operation is critical to establishing and maintaining flow.
Standardize equipment maintenance with log sheets and checklists.

## Slide 36: Push Vs. Pull Systems
Push System - Resources are provided to the consumer based on forecasts or schedules
Pull System – Controls the flow of resources by replacing only what has been consumed
Consists of:
Production based on actual consumption
Small lots
Low inventories
Management by sight
Better communication

## Slide 37: Pull System Flow Diagram
Supplier
Raw
Material
Process
A
Process
B
Finished
Goods
Kanban Locations
(signal)
Process
C
Customer
Part Flow
Information Flow
X
X
Notes: TIME: Max ___ minutes
PURPOSE: Demonstrate how a pull system works
KEY POINTS:
  1. Production precision based on actual consumption 2. Small lots or 1 piece flow 3. Low inventories 4. Waste reduction 5. Management by site – visual controls 6. Improved communication
It is a flexible and simple method of controlling and balancing the flow of resources based on what is consumed
Pull is focused on eliminating waste of handling, storage, expediting, obsolescence, repair, rework, facilities, equipment and excess inventories (WIP & FG)
  Flow diagram shows 1. customer pulls from finished goods 2. Finished goods sends an information signal to process C 3. Process C replenishes Finished goods 4. Pulls WIP and adds value 5. Information signal from Process C alerts Process B for replenishment 6. Process B replenishes C’s buffer 7. Process B pulls WIP and adds value 8. Information signal from B alerts Process A 9. Process A replenishes B’s buffer 10.Process A pulls raw material from raw material 11.Information goes to the supplier to replenish 12.Supplier replenishes the raw material
QUESTIONS:
TRANSITIONS:

## Slide 38: Value Stream Mapping
FI FO
Dealer
Network
(customers)
800 / month
Daily
Kitting
Frame &
Fuel Tanks
Axles &
Cooling Sys.
Cab &
Bumpers
Windscreen
& Cab Final
Wheel
Installation
CT = 9 sec
FTTQ = 100%
CO = 10 sec
batch = 5
O
.
= 2
CT = 11 sec
FTTQ = 100%
CO = 20 sec
batch = 5
= 1
CT = 13 sec
FTTQ = 40%
CO = 20 sec
batch = 5
CT = 26 sec
FTTQ = 100%
CO = 20 sec
batch = 5
= 1
CT = 15 sec
FTTQ = 100%
CO = 20 sec
batch = 5
= 1
CT = 9 sec
FTTQ = 100%
CO = 20 sec
batch = 5
= 1
CT = 6 sec
FTTQ = 40%
CO = 0 sec
= 1
= 1
O
.
O
.
O
.
O
.
O
.
O
.
I
I
I
I
I
I
35 trucks
5 trucks
5.0 days
5 trucks
15 trucks
15 trucks
10 trucks
Michigan
Steel Co.
Tues &
Thurs
Production
Control
Daily Ship Schedule
Daily
Order
30/60/90 day
Forecast
Weekly Schedule
MRP
6-week
Forecast
Weekly
Fax
.13 days
.38 days
.88 days
.13 days
.25 days
.38 days
.13 days
5.0 days
.38 days
.88 days
.13 days
.38 days
.25 days
9 seconds
11 seconds
13 seconds
26 seconds
15 seconds
9 seconds
6 seconds
93 seconds
7.15 days
Production
Lead Time =
Processing
Time =
40 trucks / day
Great Northern
Trucking Company
Date
Current State
Final Insp.

## Slide 39: Step 2: Establish takt Time
Takt Time = Demand Rate =
Available Work Time
Customer Demand
600 Seconds
40 Trucks
Takt Time =
= 15.0 Sec/truck
Cycle Time (Length of Individual Processes)
Takt Time
Minimum # of People
Needed per Process
=
GOAL: PRODUCE TO DEMAND
Notes: Purpose: Demonstrate how to calculate Takt Time
Main point:
Takt time sets the pace for the cell. It is how often 1 part should come off of the end of the line
Smooth and steady is the goal.
The goal is to produce to the demand

## Slide 40: Unevenness
Unbalanced Line
Operation
Balanced Line
Operation
Takt Time = 15 seconds
Notes: Purpose: Demonstrate line balancing
Main point:
Don’t focus on materials, distribute the work evenly between operators to achieve a balanced line.
Each operation in the process must be less than or equal to the Takt time.

## Slide 41: Overburden
Chart: 
| REQUIREMENTS
REASONABLE CAPACITY/ CAPABILITY OF PEOPLE OR EQUIPMENT | 10 | 10
COMPANY REQUIREMENTS

## Slide 42: Overburden, Waste, and Unevenness
UNEVENNESS
OVERBURDEN
8 WASTES
Responsible for most organizational inefficiencies

## Slide 43: Simulation Round 3
What Improvements
Would you like to
Implement?

## Slide 44
Lean Tools
Value Stream Mapping
Pull and Flow Systems
Sort, Set In Order, Shine, Standardize, Sustain (5S)
Point of Use Storage (POUS)
Batch Size Reduction
Visual Controls (Kanban)
Standard Work
Workload Balance Chart and TAKT
Layout Improvement
How many
did you get ?

## Slide 45
De-Brief &
Disassemble
How did it feel?
What can we do better? How?
How did we do financially?

## Slide 46: Different Production Environments
Lean is for all types of manufacturing companies
Low Volume
High Volume
Medium Volume

## Slide 47: Traditional Vs. Lean
Traditional manufacturing is hard on people
Lean manufacturing is hard on process

## Slide 48: Why Bother?
Lead Time Reduction
0% 25% 50% 75% 100%
Productivity Increase
WIP Reduction
Quality Improvement
Space Utilization
Typical Results Achieved

## Slide 49: Looking Forward
Use Value Stream Mapping
We will use Current State – Future State analysis to plot a course for lean activities utilizing VSM as first step.
An incremental “Plan-Do-Check-Adjust” (PDCA) approach will be used to navigate between the current state and future state workplace.
Creative “PDCA” thinking thrives on an experimental mindset, a willingness to challenge our assumptions and ability learn from our mistakes as we go.

## Slide 50: Resolve to TRY the new process & procedures
Why, that’s
impossible!
If only it were
that easy!
Are you saying
we’re doing it
wrong now?
We would be
laughed at for
trying that!
We tried that
before and it
didn’t work.
We don’t do
things that
way here.
That will
take longer
than it does
now!
It’s too
radical!
That’s a
stupid idea!
The computer
won’t let us
do that!
Our products
are different!
Notes: Purpose: Don’t make excuses
Main point:
Drive home the point that it is not a simple process
You will have to work through a lot of preconceived notions to make this successful.

## Slide 51
Questions

## Slide 52: Thank You!
Instructor Name
Oregon Manufacturing Extension Partnership
Email
www.omep.org